## Slide 1: MCM6000 Master Controller Module 7 Slots Last Update: 3/14/2018

## Slide 2: System Task
Below are function calls from USB device task
Supervisor Task
(10ms/0)
Check Power, and temperatures
Check Cables
Service Status LED
USB Host Task (100ms/0)
Check connections and add or remove device task
Check HUB for connection changes on any of it's ports
USB Device Task 0
Device task created for each new device connected
USB Device Task 1
Used for enumeration
USB Device Task 7
USB Slave Task (Interrupt/0)
Data from PC comes in by interrupt and fires a notification to the task to grab the data and store in a fifo
Parses the data and check validity
Dispatches the data to another task if necessary
Slot Card Task 1-7
Sync Motion 8
HID Poll
Read Data
Parse Controls
Dispatch to task according to control mapping
Synchronized Motion Task
Stepper Task
Servo Task
DAC Task
RS232 Task
Card Task (10ms/1)
Device task poll for new data (10ms/0)
HID Out
Request card task data
Send USB data out to control/controls
according to mapping
Init created task (interval/priority)
On the fly created task
FTDI Slave Task (100ms/0)
Same as above
Idle Task (NA/0)

## Slide 3: USB Out transfer
HID_out function:
Check if we have a map for each control on this USB device.
If we have a Control disable, don’t send HID commands from control to task.
If we have a Task disable, send a queue message to task to disable.
If we have a limit status, read the task queue, if on limit blink at 1 sec interval until limit clears.
Mapping mode:
Control disable, set on brightness and color
Task disable, set on brightness and color
Limit status , set on brightness and color and blink rate
HID_out function is called inside of the USB_device task every 10ms.

## Slide 4: USB Joystick Controls
Joystick Controls
Knobs: 16 bit in (velocity)
Large button: 1 bit in 24 bit out
Small buttons: 1 bit in 9 bit out (bit 9 red/green)
Toggle Switch: Fast/slow
In report for MCP7
Byte 15 | Byte 14 | Byte 13 | Byte 12 | Byte 11 | Byte 10 | Byte 9 | Byte 8 | Byte 7 | Byte 6 | Byte 5 | Byte 4 | Byte 3 | Byte 2 | Byte 1 | Byte 0
B6 Red | B6 Green | B5 Red | B5 Green | B4 Red | B4 Green | B4 Blue | B3 Red | B3 Green | B3 Blue | B2 Red | B2 Green | B2 Blue | B1 Red | B1 Green | B1 Blue
0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255 | 0-255
Out report for MCP7
button 5&6 only one color at a time
0 is off, 255 is full on
Byte 8 |  |  |  |  |  |  |  | Byte 7 | Byte 6 | Byte 5 | Byte 4 | Byte 3 | Byte 2 | Byte 1 | Byte 0
NA | NA | Button 6 (small bottom) | Button 5 (small top) | Button 4 (right) | Button 3 | Button 2 | Button 1 (left) | Knob 4 (16 bit, top bit direction) |  | Knob 3 (16 bit, top bit direction) |  | Knob 2 (16 bit, top bit direction) |  | Knob 1 (16 bit, top bit direction) | 
0 | 0 | 0-1 | 0-1 | 0-1 | 0-1 | 0-1 | 0-1 | -32767 to 32767 |  | -32767 to 32767 |  | -32767 to 32767 |  | -32767 to 32767 | 

## Slide 5: USB out transfer mapping
Joystick 1
RGB LED 1
RGB LED 2
RGB LED 3
Joystick 2
LED 1
LED 2
LED 3
Slot 1 task
Slot 2 task
Slot 2 task
Map Example RGB
Port - J1
Type – Generic Indicator
Mode – (limit(blink red), disable control (orange), disable task (red), moving(green), stopped (off)). These are all bits colors are not configurable.
Slot - 1
Brightness is global and set with a command a
Map Example LED
Port - J1
Type – LED
Mode – (limit(blink red), disable control (red), disable task (red), moving(off), stopped (off)).
Slot - 1

## Slide 6: USB Joystick Speed
Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
High speed 0 – 16 |  |  |  | Low speed 0 - 16 |  |  |