## Slide 1
LED
TOOLBOX
CPLD TOP
STEPPER
CARDS
Chip Select
7 x Encoder
7 x PWM
Clocks
SPI
Wishbone
Servo
FAN
OW_DET
AD5624 DAC
QUAD DAC (GALVOS)
RS232

## Slide 2
All additions to this project should be added here for clarity but also so a place for others to see what's available for reuse.
All card modules need to be able to be commented out for compile time without breaking anything so that as more logic is required for different system, there should be an easy way to comment out modules that particular system doesn't need.
Special function modules can be created but must also be able to be commented out.
All modules are disabled after reset except for LED
uC firmware should have a separate top file for each module.

## Slide 3
12MHz from uC (pin 104)
Clocks Module
IO’s
CLK_38MHz
Clocks out
CLK_12MHz
Internal Clock
(need before programming)
CLK_1MHz_PLL
CLK_120MHz_PLL
CLK_400MHz_PLL
CLK_500KHz_PLL
CLK_25KHz_PLL
CLK_48MHz_PLL
Clock used for modules should be selected to minimize logic i.e. PWM for should use a slower clock so the compare register for the duty cycle is as small as possible

## Slide 4
LED_OUT (pin 126)
LED Module
Using internal instantiated PWM
[SET]
LED_SET_PWM_DUTY: 0 off, 255 full on
IO’s to Slot
CLK_25KHz_PLL
CLOCKS IN

## Slide 5
FAN_OUT (pin 82)
Fan Module
IO’s to Slot
CLK_25KHz_PLL
CLOCKS IN
Using internal instantiated PWM
[SET]
FAN_SET_PWM_DUTY: 0 off, 255 full on

## Slide 6
CS_0
Chip Select Module
IO’s
CLK_400MHz_PLL
CLOCKS IN
CS_1
CS_2
CS_3
CS_4
CS Pin to slot | Value | CS_4 | CS_3 | CS_2 | CS_1 | CS_0
CS_ALL_HIGH | 0 | 0 | 0 | 0 | 0 | 0
Slot 1 CS 1 | 1 | 0 | 0 | 0 | 0 | 1
Slot 1 CS 2 | 2 | 0 | 0 | 0 | 1 | 0
Slot 2 CS 1 | 3 | 0 | 0 | 0 | 1 | 1
Slot 2 CS 2 | 4 | 0 | 0 | 1 | 0 | 0
Slot 3 CS 1 | 5 | 0 | 0 | 1 | 0 | 1
Slot 3 CS 2 | 6 | 0 | 0 | 1 | 1 | 0
Slot 4 CS 1 | 7 | 0 | 0 | 1 | 1 | 1
Slot 4 CS 2 | 8 | 0 | 1 | 0 | 0 | 0
Slot 5 CS 1 | 9 | 0 | 1 | 0 | 0 | 1
Slot 5 CS 2 | 10 | 0 | 1 | 0 | 1 | 0
Slot 6 CS 1 | 11 | 0 | 1 | 0 | 1 | 1
Slot 6 CS 2 | 12 | 0 | 1 | 1 | 0 | 0
Slot 7 CS 1 | 13 | 0 | 1 | 1 | 0 | 1
Slot 7 CS 2 | 14 | 0 | 1 | 1 | 1 | 0
EEPROM | 15 | 0 | 1 | 1 | 1 | 1
MAX3421 | 16 | 1 | 0 | 0 | 0 | 0
CS1_1_REG
CS1_2_REG
CS2_1_REG
CS2_2_REG
CS3_2_REG
CS4_1_REG
CS4_2_REG
CS3_1_REG
CS5_1_REG
CS5_2_REG
CS6_1_REG
CS6_2_REG
CS7_2_REG
CS_EEPROM_PIN
CS_MAX6421_PIN
CS7_1_REG
Up to 32 CS

## Slide 7
CM_2(pin 107)
OW_DET Module
Used for cable detection, just routs the OW_ID pin from slot to uC through pin
CM _2
IO’s to Slot
CLK_???Hz_PLL
CLOCKS IN
OW_ID_PIN (pin from slot)
REGS IN

## Slide 8
CHA _WIRE_IN
CHB _WIRE_IN
UL_WIRE_IN
LL_WIRE_IN
ENCODER Module
INDEX_WIRE_IN
IO’s to Slot
Regs
[SET]
ENC_ENABLE: 1 enabled, 0 disabled
ENC_LIMITS: HAS_UL | HAS_LL | HAS_INDEX
ENC_ZOL (zero on limit): 1 enbled, 0 disabled
ENC_SET_COUNTS: 32bits LSB
[GET]
ENC_GET_COUNTS: 32bits LSB
ENC_READ_INTERRUPT: UL| LL | INDEX
[INTERRUPT]
Interrupt on all edges of enabled limits, clear when read, debounce done on uC.
SPI 2nd byte specifies interrupt source i.e. ENCODER because there may be other source for slot interrupts.
INT_1 : INT_7
REGS OUT
ENC_COUNT_CLK (used for
constant velocity)
IO’s to uC
CLK_400MHz_PLL
CLOCKS IN

## Slide 9
PWM_WIRE_OUT
PWM Module
IO’s to Slot
Regs
[SET]
PWM_ENABLE: 1 enabled, 0 disabled
PWM_SET_PWM_FREQ: 32bit value
PWM_SET_PWM_DUTY: 32bit value
REGS IN
PWM_DUTY: 32bits
CLK_120MHz_PLL
CLOCKS IN
PWM_WIRE_IN

## Slide 10
C1: RESET
C5: OW_ID (cable det)
C7: STCK (step clock not used)
Stepper Module
Regs
[SET]
STEP_ENABLE: 2 enbled, 1 connects only OW_ID, 0 disabled ( connects IO to other modules when enabled or tri-states if disabled)
STEP_RESET: 1 HIGH, 0 LOW
STEP_STCK: 1 HIGH, 0 LOW
IO’s to Slot
May use Encoder Moudule
CLK_400MHz_PLL
CLOCKS IN
CHA _REG_OUT
CHB _REG_OUT
UL_REG_OUT
LL_REG_OUT
INDEX_REG_OUT
C8: CHA
C9: CHB
C2: UL
C3: LL
C4: INDEX
C6: CS
Map IO to encoder on
card enable
CSX_1_REG

## Slide 11
C0: MODE2
C3: FAULT
C4: MODE1
Servo Module
Regs
[SET]
SERVO_ENABLE: 2 enbled, 1 connects only OW_ID, 0 disabled ( connects IO to other modules when enabled or tri-states if disabled)
SERVO_MODE: 0 PWM_ONLY, 1 SHUTTER, 2 CONT_VEL
SERVO_MODE_PINS: MODE2 | MODE1
SERVO_DIR: 1 high, 0 low
SERVO_OW_ID: 1 tie to pin CM_2, 0 Tristate
SERVO_SET_CONST_VEL: 32bit value to compare ENC_COUNT_CLK to 120MHz clock to modulate the PWM_DUTY
[GET]
SERVO_READ_FAULT:
IO’s to Slot
C5: DIR (Phase)
C6: OW_ID (cable det)
C7: ENABLE (PWM)
May use Encoder module
Uses PWM module
ENC_COUNT_CLK (used for
constant velocity)
REGS OUT
PWM_DUTY: 32bits
CLK_400MHz_PLL
CLOCKS IN
CLK_120MHz_PLL
CHA _REG_OUT
CHB _REG_OUT
UL_REG_OUT
LL_REG_OUT
INDEX_REG_OUT
C8: CHA
C9: CHB
C2: UL
Map IO to encoder on
card enable
PWM_REG_OUT
PWM_REG_IN

## Slide 12
C1: -
C5: -
C7: LASER_CNTRL
AD5624 DAC Module
Regs
[SET]
AD5624_ENABLE: 1 enbled, 0 disabled ( connects IO to other modules when enabled or tri-states if disabled)
AD5624_ LASER_CNTRL : 1 enabled, 0 disabled
AD5624_ IPG_B_REFL : 1 enabled, 0 disabled
IO’s to Slot
CLK_48MHz_PLL
CLOCKS IN
C8: -
C9: IPG_B_REFL
C2: -
C3: -
C4: -
C6: -
CSX_1_REG
Map IO to chip select
C0: CS
On OTM 41-0094 only on slot 4

## Slide 13
C1: VERT_SYNC
C5: TGP
C7: CS_LD
QUAD DAC Module
Regs
[SET]
AD5624_ENABLE: 1 enbled, 0 disabled ( connects IO to other modules when enabled or tri-states if disabled)
AD5624_ LASER_CNTRL : 1 enabled, 0 disabled
AD5624_ IPG_B_REFL : 1 enabled, 0 disabled
AD5624_CLEAR_RAM : (92Kbits or 11.5k bytes of EBR SRAM)
AD5624_WRITE_RAM :
AD5624_SCAN_RATE: 32bit
AD5624_CNTRL_MODE: 0 direct, 1 EBR lookup
Galvo Pattern:
1024 x 1024 resolution on screen x 16 bit value for DAC
Start / stop vectors per line are calculated on PC and sent down to uC through USB, then the data is loaded to EBR through SPI from the uC to CPLD
RAM required: 1024 (lines) x 2 (bytes start) x 2 (bytes end) = 4,096 bytes
Paths are calculated in CPLD to provide linear scans with fastest turnaround time possible
IO’s to Slot
CLK_48MHz_PLL
CLOCKS IN
C8: OVERTMP
C9: SYNC_IN (res scanner)
C2: DAC_SCK
C3: DAC_SDO
C4: DAC_SDI
C6: HORZ_SYNC
CSX_1_REG
C0: LDAC
SPI SUB Module
On OTM 41-0094 only on slots 6 & 7 using LTC2664CUH-16#PBF for Galvos but can be used for other applications

## Slide 14
C1:RX-
C5: -
C7: -
RS232 Module
Regs
[SET]
X_ENABLE: 1 enabled, 0 disabled, ( connects IO to other modules when enabled or tri-states if disabled)
also routes RX TX to uC dedicated CPLD RX TX
[GET]
IO’s to Slot
CLK_48MHz_PLL
CLOCKS IN
C8: -
C9: -
C2: -
C3: -
C4: -
C6: -
-
C0: TX
On OTM 41-0094 only on slot 5

## Slide 15
C1: -
C5: -
C7: -
Template Module
Regs
[SET]
X_ENABLE: 1 enabled, 0 disabled ( connects IO to other modules when enabled or tri-states if disabled)
[GET]
IO’s to Slot
CLK_48MHz_PLL
CLOCKS IN
C8: -
C9: -
C2: -
C3: -
C4: -
C6: -
-
C0: -